## Slide 1
Group: B.Sc. III Year
Subject: Electronics
Semester: 5
Paper : 5
w.e.f. 2018 - 19 ADMITTED BATCH
Title of the paper: Microprocessor (Intel 8085)
P.R. GOVERNMENT COLLEGE (A), KAKINADA

## Slide 2
Topic : Pin description of 8085 Microprocessor

## Slide 3
8085 Pin Diagram

## Slide 4
The 8085 is an 8-bit general purpose microprocessor capable of addressing 64 k of memory.
This device has 40 pins requires a +5 V power supply and can operate with a 3 MHz single phase clock.

## Slide 5
All the signals are classified into 7 groups:
  Address bus
  Data bus
  Control & status signals
  Power supply and frequency signals
  Externally initiated signals
  Serial I/O signals
  Interrupt signals
Classification of Signals

## Slide 6
The 8085 has 8 signal lines from A8 – A15 which are unidirectional and used as higher order address bus.
Address Bus
The signal lines from AD7 – AD0 are bidirectional, they serve for a dual purpose.
They are used as the lower order address bus as well as the data bus.
Multiplexed Address & Data bus

## Slide 7
This group of signals includes two control signals and , three status signal IO/, S1 and S0.
To identify the nature of operation one special signal ALE is used to indicate the beginning of the program.
(Read): This is a read control signal (active low). This signal indicates that the selected IO or memory device is to be read and are available on the data bus.
(write): This is a write control signal (active low). This signal indicates that the data on the data bus are to be written into a selected memory of IO location.
Control and Status signals

## Slide 8
This is a status signal used to differentiate between IO and memory operations.
When it is high it indicates an IO operation, when it is low it indicates an memory operation.
This signal is combined with read and write to generate IO and memory control signals.
S1 and S0 indicate the type of machine cycle in progress.
IO/, S1 and S0

## Slide 9
It is an output signal used to give information of AD0-AD7 contents.
This is a positive going pulse generated any time the 8085 begins its operation.
When pulse goes high it indicates that AD0-AD7 lines are address.
When it is low it indicates that the contents are data.
This signal is used primarily to latch the lower order address from the multiplexed bus and generate a separate set of 8 bit address lines.
ALE(Address Latch Enable)

## Slide 10
  Vcc: +5 V DC power supply
  Vss: Ground reference
  X1, X2: A crystal is connected at these two pins having frequency of 6 MHz. The frequency is internally divided by 2.
  CLK Out: Clock output signal can be used as the system clock for the other devices.
Power supply and clock frequency